## Preferred Energy Compaction Schemes
It was found that the best compression so far had been achieved with the DWT, with the DCT being next best. It was decided to shortlist three schemes for further consideration, in order to allow flexibility when choosing a final scheme.
1. 8x8 DCT, step size = 24, CR ~ 2.98
2. 32x32 DCT, step size = 21, CR ~ 2.79
3. 5 level DWT, k = 0.8, delta = 12, CR ~ 3.10
## Centre-Clipped Linear Quantisers
When quantising an energy compacted image, many of the sub-images (those representing highpass and bandpass components) contain coefficients near to zero. Quantising as many of these as possible to zero increases the amount of compression which can be achieved. One way to do this is to skew the quantisation boundaries such that more coefficients are mapped to zero than would be under a uniform scheme. Various widths of `zero' step were used. For each of the preferred schemes, the effect of changing the `rise' variable was investigated.
	Rise (/step)	Step Size	rms Error	Compression Ratio
8x8 DCT	0.5	24	4.9103	3.07
	0.9	17	4.9299	3.20
	1.0	16	5.0257	3.26
	1.1	15	5.0847	3.39
	1.5	11	4.9438	3.18
32x32 DCT	0.5	21	4.8892	2.78
	1.0	14	5.0678	3.18
	1.5	9	4.7294	2.89
	Rise (/steps)	Delta	rms Error	Compression Ratio
5 Level DWT	0.5	13	4.9894	3.22
	1.0	8	4.8152	3.26
	1.5	6	5.0334	3.27
	2.0	4.5	4.9638	3.48
	3.0	3	4.9170	3.02

Table 1: Effect of varying rise on achievable compression. Preferred rise highlighted.
It was found that the DCT had an optimum compression ratio when `rise' was slightly greater than 1.0. Given the small differences in compression ratio at small deviations from the optimum, it is reasonable to assume that taking `rise' to be equal to the step size will return an acceptably high compression ratio. Choosing this value allows the same quantiser to be used for different sizes of DCT block.
The DWT performs more energy compaction, that is, the highpass and bandpass sub-images contain lower energy than their DCT equivalents. This means a higher rise value can be used without losing too much information, and thus affecting the rms error. A value of twice the steps vector was found to be suitable. It would be acceptable to use a rise coefficient of 1.0 for the DWT, but there does not seem to be much point in choosing the same standard as for the DCT, since other aspects of the compression algorithm are very different.
### Suppression of Sub-images
#### DCT
Various ways of suppressing sub-images were considered. For the 8x8 DCT scheme, the most highpass half of the coefficients (i.e. the bottom right triangle of each DCT block) were set to zero.
	rms Error	Compression Ratio
Basic DCT	5.0307	3.26
Half Highpass Coefficients Suppressed	9.3981	4.53

Table 2: Effect on compression ratio of suppressing the most highpass half of the DCT coefficients
The numbers in Table 2 and the images in Figure 1 show the benefit of this approach. The amount of blurring is slightly increased, as would be expected when high frequency information is lost, but the degradation in quality is not unacceptable, while the increase in compression ratio is significant.
The increase in rms error is inevitable with this process, as genuine differences from the original are being introduced around high frequency components. This increase in error is unavoidable, as even reducing the quantisation step size to 1 only brings the error down to ~8.6. This is more a limitation of using rms error to quantify image quality than a problem with the compression - the high frequency-suppressed image is not of greatly worse subjective quality.
By contrast, if the quantisation of the normal DCT image is increased such that it's compression ratio is now ~4.5, the subjective quality is much worse, although the rms error is only 6.63. The high frequencies are slightly improved over the highpass-suppressed image.
Figure 1: Left: half the highpass coefficients suppressed. Right: basic DCT
#### DWT
The DWT produces three highpass images and one lowpass on every level. Of these, the directionless highpass image is clearly of very low energy (it appears almost entirely grey / i.e. most coefficients are zero), and the other two highpass images are of somewhat higher energy. Three supression schemes were tried:
1. The top level directionless highpass sub-image was suppressed.
2. All three top level highpass sub-images were suppressed.
3. All five directionless highpass sub-images in a five level DWT were suppressed.
Of these, scheme (1) produced an image which was indistinguishable from the basic DWT reference, with a predictably modest improvement in compression.
	rms Error	Compression Ratio
DWT reference	4.9638	3.48
1. top level directionless highpass sub-image	5.5046	3.61
2. all three top level highpass sub-images	15.8537	8.09
3. all five directionless highpass sub-images	10.7711	3.94

Table 3: Compression achievable when suppressing various sub-images in a DWT
The effect of the suppression schemes are shown in Table 3. Scheme (2) produced an unusable reconstructed image - suppressing the vertical and horizontal high frequencies was too severe.
The effect of scheme (3) is seen in Figure 2 - mostly edges themselves are unaffected, but an ethereal aliasing effect distorts the image around the edges. This could be due to the effect of small errors introduced by suppression of the lowest sub-image being propagated and magnified by suppression of all the subsequent sub-images. The resulting image quality was considered too poor for scheme (3) to be a viable compression method.
Figure 2: Left: suppression scheme (3) - all directionless highpass sub-images removed. Right: reference DWT
## Huffman Coding
The energy compacted and quantised image can be further (losslessly) compressed for transmission by encoding the bit stream. Since the bit stream contains many zeros with occasional non-zero coefficients, Huffman encoding can be used to compress this. One of the factors which can be varied is choosing the ordering of image coefficients which are fed into the encoder to optimise the statistics of the coefficient stream. Huffman encoding produces the best results when non-zero coefficients are widely spaced (i.e. with as many zeros between them as possible), or as close together as possible (ideally with no zeros between them), because the shortest Huffman codewords can then be used most often for runs of non-zero coefficients, and long runs of zeros can be efficiently transmitted by the run-of-16-zeros codeword.
DCT sub-images have the DC coefficient in the top left corner, and then coefficients become increasingly high frequency towards the bottom right. A zig-zag scan of the subimage can thus be used to order the coefficients by increasing frequency, maximising the likelihood of achieving the above-stated ideal distribution.
To decode the bit stream, the codewords used for encoding must be known. This can be achieved by using a standard table at both ends, or a custom table optimised for the specific image being encoded, and transmitted along with the image to the decoder. The standard JPEG table is designed for 8x8 DCT images with a zig-zag coefficient ordering. Therefore if this scheme is used, the standard tables form a good fit (i.e. a custom table might not achieve much better compression), and can be used, saving the cost of sending a custom table. Any variations on the compression scheme (e.g. using DWT, or a combination of DCT and DWT), will significantly change the characteristics of the coefficient stream, and thus the standard JPEG table will not be able to encode it efficiently. Thus a custom table is necessary (or a different, pre-defined, table).
## Designing The Final Compression Scheme
### Energy Compaction
Both the DCT and DWT have desirable characteristics, and it was thought that a combination of the two methods could provide the advantages of both. A purely DCT compressed image contains noticeable blocky artaefacts when it has been severely compressed. The smoothing effect of quantising a DWT compressed image can be used to soften these features if a DWT is performed first. That said, the greatest gains in compression ratio (while retaining an acceptable reconstructed image) were achieved by suppressing DCT coefficients (cf Tables 2 and 3).
### Coefficient Suppression
A scheme of one level of DWT compaction, followed by an 8x8 DCT on the resulting low frequency sub-image was planned. The directionless high frequency sub-image from the DWT can be suppressed, which has an effectively negligible impact on the quality of the reconstructed image, but provides a small, yet useful improvement in compression ratio.
The relevance of the compression ratio to the final scheme is that the greater the compression ratio, the less quantisation of the compacted image is needed to achieve the required 40960 bit size for the compressed image.
The 8x8 DCT on the lowpass sub-image can be treated in a similar way to before - the high pass coefficients can be suppressed. The number of these coefficients which are suppressed can be varied to find a suitable compromise between image quality and compression ratio. The way the coefficients were suppressed was to draw a diagonal line from the bottom left to top right of each DCT block and set every coefficient below that (i.e. of higher frequency than those above the line) to zero. The position of this line was defined as an offset from the longest possible diagonal, which would cause half of the coefficients to be suppressed. It was found that starting the suppression four rows below this resulted in an acceptable image quality. In an 8x8 DCT, this results in 15 out of every 64 coefficients being suppressed.